## Slide 1
Smart Cards and
Java Card Programming
Java Card 3.0 Programming
Stephane Chretien
stephane.chretien@gemalto.com

## Slide 2: Presentation objectives
•
Introducing the concepts and the technology of the smart cards
Describing the protocols between cards and terminals
Describing how to program the Java Cards
Exploring the tools and the environments provided by the manufacturers to develop solutions with smart cards
Java Card 3.0 Programming

## Slide 3: Presentation content
Introduction
ISO7816 Protocol
Java Card
The basic rules for Java Card programming
Cyphering
SIM Card
Smart Card Web Server
Java Card 3.0 Connected Edition
Conclusion
Java Card 3.0 Programming

## Slide 4: Introduction
Java Card 3.0 Programming
History, technology, standards

## Slide 5: Introduction
Java Card 3.0 Programming
●
In this chapter, we'll see
●
●
●
A brief history of the smart cards
The applications supported by the smart cards The standards supported

## Slide 6: Brief history
Early seventies, first patents
  Dr Arimura, R Moreno, M Ugon
Early eighties, first field testing for a memory card
  Phone card in France
Mid eighties, large scale introduction of smart cards in banking system
Mid nineties, SIM card introduced in mobile telephony
End nineties, VITAL card introduced in france
Java Card 3.0 Programming
Notes: 1976 la 1er carte a puce microcircuit est developpe : Bull
1978 la 1er carte avec micro-pro
Pouvoir francais on soutenu deux project
  Carte bancaire=> EMV
  Carte telephonique => PTT

## Slide 7: What is a smart card
A plastic card like a credit card with an embedded micro chip
  With or without visible contacts
    Maybe contactless
Standardized
– ISO 7816
Mecanical properties
Electrical behavior
Communication protocol
Contains a software which
  Protects internal data (Keys, Money, ..)
  Give access to these data in a secure way  Authentication (PIN, …)
  Perform sensitive and cryptographic operation
Java Card 3.0 Programming

## Slide 8: For what applications …
Payment (ePurse, EMV)
Loyalty systems
Access control
Telephony
- Mobile (GSM …)
e-Government
– ID card, passport
File system
  Health (carte vital)
  Education
– …
Java Card 3.0 Programming

## Slide 9: Architecture
CPU
ROM
(Operating System)
RAM
(temp / transient storage)
NVM / EEPROM / FLASH
(application storage)
UART
(I/O System)
reset
CLK
I/O
VCC
Crypto
CPU : 8/16/32 Bits from 3.57Mhz to 24Mhz
RAM : 1KB to 24KB
NVM : few KB of EEPROM to 128MB of NAND Flash

## Slide 10: Standards
• ISO 7816
• GSM 11.11 V6.1.0
• GSM 11.14 V7.1.0
- SIM Toolkit specs
• GSM 03.19 V1.0.0
- SIM API for Javacard
ETSI
– TS 31 130
– TS 102 241
– TS 102 588
Java Card
  Java Card Forum
EMV
  Europay, Mastercard, Visa
Global Platform
Java Card 3.0 Programming
Notes: 11.11 => SIM and high level description of command
11.14 => allow interaction with end user
03.19 => SIM API Javacard specification
102 241 =>

## Slide 11: Standards
Java Card 3.0 Programming
SIM = Subscriber Identity Module  GSM standard
USIM = Universal Subscriber Identity Module 3G, LTE,..
UICC = Universal Integrated Circuit Card  a smartcard

## Slide 12: Conclusion
Java Card 3.0 Programming
●
In this chapter, we have seen
●
●
●
A brief history of the smart cards
The applications supported by the smart cards The standards supported

## Slide 13: ISO7816 Protocol
Java Card 3.0 Programming
Physical description, communication layer,
file system

## Slide 14: Introduction
An introduction to the ISO7816 standard
What is an APDU
How to exchange data between the CAD and the smart card
Java Card 3.0 Programming
●
In this chapter, we'll see

## Slide 15: Mechanical and Electrical Aspects
ISO 7816 standard describes
  Physical and Electrical characteristics
  Transmission protocol
  Security and Command exchange
  File System
  …
Possible power voltage
  3V or 5V
  Lower maybe in the future
Clock
Java Card 3.0 Programming

## Slide 16: USB and NFC port
●
Added to the SIM card standard
●
●
A USB port in place of the two optionnal contacts on the bottom of the circuit
A NFC (Single Wire Protocol) port for the last optionnal contact
USB Port
NFC SWP
Java Card 3.0 Programming
NFC = Near Field Communication

## Slide 17: Half-duplex serial protocol
Due to the unique pin dedicated to input/output, the first protocol used by the smart cards were
  Serial
  Half-duplex
Communication characteristics:
  Data: 8 bits
  Parity: even
  Stop: 1 bit
Speed starting at 9600 Bps to 115200 Bps
C0 00 00 02 10 00
Java Card 3.0 Programming
Input / Output

## Slide 18: USB IC
ETSI TS 102.600
●
●
Max speed 12 Mb/s Three flavours:
●
Integrated Circuit Card Devices
–
●
Compatible with the previous serial protocol
Mass Storage
–
Disk emulation
●
Ethernet Emulation Mode
–
To support TCP/IP protocol
Java Card 3.0 Programming

## Slide 19: NFC SWP
ETSI TS 1002.613 & 622
●
●
Single Wire Protocol Full duplex
●
Current and voltage modulation
●
●
Max speed 1.6 Mb/s
The smart card can act as
●
●
A RFID tag
A RFID tag reader
Java Card 3.0 Programming

## Slide 20: Terminology
The smart card reader powered by
  a PC
  a cash register
  a mobile phone
is called a terminal
In the standard ISO 7816 it is called :
  The Card Acceptance Device
  Or CAD
Java Card 3.0 Programming

## Slide 21: Answer to Reset
When a card is inserted into the reader, a micro-switch signals this event to the terminal.
The terminal powers up the card
– Using a particular protocol
When it is properly powered, the card sends back to the terminal a message called "Answer to Reset"
Java Card 3.0 Programming
reader
Smartcard
Power up
Answer to Reset
Supported protocol
Supported Voltage
Speed
Type of card
Card manufacturer

## Slide 22: General protocol
After sending Answer to Reset, the card waits until the terminal starts a communication
The card never starts a communication
The card answers to a demand coming from the terminal and waits for the next demand
The receive a APDU Command and respond with APDU Response
APDU = Application Protocol Data Unit
Java Card 3.0 Programming
reader
Smartcard
APDU Command
APDU Response
Wait for next
command
Execute
command
APDU Command = Header + Data
APDU Response = Data + Status Word

## Slide 23: Application Protocol Data Unit Command
Java Card 3.0 Programming
The APDUs are the commands sent by the terminal to the smart card
The APDU can
  Carry optionaly data to the card, Max : 255 bytes
  Expect results from the card
Card and terminal must synchronize to
  The number of bytes to exchange
  The direction of the exchange
    This is done by the software embedded in each device
CLA
INS
P1
P2
LC
LE
Header
of
5 bytes
DATA
Body Data
Of
LC bytes

## Slide 24: Application Protocol Data Unit
Class of the APDU: one byte which is caracteristic of the APDU of the application
Instruction: this is the command
P1, P2: two parameters which can be combined to form a short integer
LC: length of data which will be exchanged between the terminal and the card (from the ter- minal to the card, or from the card to the terminal)
Java Card 3.0 Programming
CLA
INS
P1
P2
LC
LE
DATA
LE: length of data Excepected which will be exchanged between the card and the terminal (only in case LC is provided)

## Slide 25: Application Protocol Data Unit Response
Carry optionally Data, Max 256 bytes
SW1SW2 is the Status Word
  report the result of the operation done by the card
  SW1=0x90 SW2 =0x00 means success!
  When different, could indicate
    Denied access
    File not found
    No such CLA or INS expected
  – …
0x9000
Java Card 3.0 Programming
SW1
SW2
Response
Body
Of
LE bytes
DATA

## Slide 26: Case 1 : No Data Exchanged
reader
Smartcard
CLA|INS|P1|P2|00
SW1|SW2
Wait for next
command
Execute
command
• LC ==0
The card receives the APDU header only
It processes it
It returns a status word
– Two bytes

## Slide 27: Case 2: Data Sent by Terminal
reader
Smartcard
CLA|INS|P1|P2|LC
SW1|SW2
Wait for next
command
Execute
command
LC  0
LC indicates the length of the data in bytes
The software in the terminal and the software in the card must agree on the direction of the exchange
The card acknowledges by sending back the INS byte
– Simple case
INS
DATA

## Slide 28: Case 3: Data Sent by Card
reader
Smartcard
CLA|INS|P1|P2|LE
SW1|SW2
Wait for next
command
Execute
command
LE  0
  The 5th byte is called LE in this case
The card acknowledges the APDU by sending back the INS byte
  Simple case
Data are returned by the card, followed by the status word
INS
DATA

## Slide 29: Conclusion
An introduction to the ISO7816 standard What is an APDU
How to exchange data between the CAD and the smart card
Java Card 3.0 Programming
●
In this chapter, we have seen
●
●
●

## Slide 30: Cours 2 : Java Card
Java Card Forum, history of the versions, programming aspects
Java Card 3.0 Programming

## Slide 31: Introduction
Java Card 3.0 Programming
●
In this chapter, we'll see
●
●
●
●
●
An introduction to the Java Card system What is a Java Card Applet
What is the Java Card Runtime Environment The lifecycle of an Applet
How to protect access with an OwnerPIN

## Slide 32: Operating systems
•
Beginning: proprietary systems
  Only the applications were standardized
    B0' for French banking system
Now: multi-application systems
  MULTOS
  Java Card
Java Card 3.0 Programming

## Slide 33: Java Card History
Early 1996
  First development
    Schlumberger, Bull CP8, GemPlus, Sun
  Schlumberger's Cyberflex
  Java Card Forum
    Most of the smart cards manufacturers
    Sun
– As a Java guru
Java Card 3.0 Programming

## Slide 34: Why Java in a smart card
•
Java is an interpreted language
– Need a Java Virtual Machine to run
Applications could be portable from one smart card to another
Applications run securely in a "sand box"
Small footprint for the applications
Java Card 3.0 Programming

## Slide 35: Is Java for Java Card pure Java?
No until Java Card 3.0!
Roughly:
  Basic types restricted to
    Boolean
    Small integers
Byte
Short
Int (optional)
No Strings
Arrays restricted to one-dimensional arrays
Limited libraries
  Including java.lang
–
No garbage collector
Less restrictions for Java Card 3.0
Java Card 3.0 Programming

## Slide 36: Which version in this course?
In this course we will introduce the Java Card 3
  Classic Edition
    Java Card 2.2.2
  Connected Edition
Java Card 3.0 Programming

## Slide 37: Available libraries
Basically, javacard and javacardx
contain the smart card API
–
framework, security and crypto
•
•
java.lang is reduced mainly to the exception definitions
java.io and java.rmi was introduced in the last 2.2 version
–
–
java.io to manage channels
java.rmi to manage remote method invocation
Java Card 3.0 Programming

## Slide 38: SIM Toolkit
For SIM Toolkit two more packages
  access
  toolkit
Will be detailed later
Java Card 3.0 Programming

## Slide 39: How Java works in a smart card
A Java Virtual Machine is embedded
  4 K bytes
  Basic library
Java Card Runtime Environment
  In charge of
    Activation and selection of applications
    Low level communication protocol
    Application downloading
Java Card Runtime Environment
Java Virtual Machine
Java Card API
Applet 1 Applet 2 Applet 3
Java Card 3.0 Programming

## Slide 40: Roles of the JCRE
Downloading a package
Creating an instance of an applet
Selecting an applet
Transmitting an APDU to a selected applet
Managing the communication protocol with the CAD
Java Card 3.0 Programming

## Slide 41: Downloading a package
Applets must be encapsulated in a package
External processes
–
Compile the applets
Verify the bytecode
Create a jar-like container
  CAP file
Will be seen later
Package and applets are associated an identifier for future selection
Java Card 3.0 Programming

## Slide 42: What is a Java Card Applet
A java object which is
  Running using the JVM
  Controlled by the JCRE
The class of this object must extend the class javacard.framework.Applet
The class must overload several methods
package ePurse;
import javacard.framework.*; class EPurse extends Applet {
short balance;
public EPurse(){…}
public static void install(…){…} public boolean select(){…} public void process(APDU apdu)
{…}
}
Java Card 3.0 Programming

## Slide 43: Class APDU
•
This class provides the basic features needed to handle the ISO7816 protocol from the applet point of view
It gives access to the internal buffer dedicated to the communication
This buffer can be
  Retrieved by the applet
  Filled up by the applet and sent to the CAD
CLA
INS
P1
P2
LC
Java Card 3.0 Programming

## Slide 44: Main methods of the APDU
•
These methods help to
  Get the internal buffer
  Start receiving data
    Acknowledgement
  Start transmitting data
Utilities help to
  Transform 2 bytes in a short and vice versa
  Copy buffers
  Compare buffers
byte buffer[] = apdu.getBuffer();
apdu.setIncomingAndReceive();
short le = apdu.setOutgoing(); apdu.setOutgoingLength(le); apdu.sendBytes(ISO7816.OFFSET_CDATA,
le);
apdu.setOutgoingAndSend(...);
Java Card 3.0 Programming

## Slide 45: Class ISO7816
This class encapsulates most of the ISO7816 constants needed to program the applets
Constants are prefixed by
  CLA for class related constants
  INS for instruction related constants
  OFFSET for offsets in the buffer
  SW for status word related constants
Java Card 3.0 Programming

## Slide 46
Java Card 3.0 Programming
MyApplet.java
MyApplet.class
Javac
MyApplet.cap
Javacard
converter
Build and load a Javacard Package
MyApplet.cap
Loader
The java applet source code is compiled and converted in a CAP file
The CAP file is a Javacard package
The CAP file is loaded in the Javacard using several specific APDU command handled by the JCRE (JavaCard Runtime Environment)

## Slide 47: Lifecycle of an applet
•
The JCRE downloads the package containing the Applet
It calls the static method
install on the Applet
This method creates an instance
– Or more
And register this instance using an AID
JCRE
Applet
install
instance
new
instance aid
register
Java Card 3.0 Programming

## Slide 48: Lifecycle of an Applet
When the instance is created and registered it can be called
The JCRE can
  select
  deselect
the instance
Can call the instance to
process an APDU
JCRE
Applet
instance
instance aid
select
Java Card 3.0 Programming
process
deselect

## Slide 49: Example of an Applet
Java Card 3.0 Programming

## Slide 50
Java Card 3.0 Programming

## Slide 51
Java Card 3.0 Programming

## Slide 52: Simulation script
Java Card 3.0 Programming

## Slide 53: Result
Java Card 3.0 Programming

## Slide 54: Netbeans
Java Card 3.0 Programming

## Slide 55: Other Java Card features
Many features available
  PIN code management
  Transaction handling using JCSystem
    Possibility to group together a certain number of actions into a transaction
    Possibility to abort or commit the transaction
  Shareable applets
  Possibility to have several applets selected at the same time
Java Card 3.0 Programming

## Slide 56: OwnerPIN
Java Card 3.0 Programming
This class helps the developer to protect the access to some features of the smart card using a PIN code
private OwnerPIN pinCode;
/** Creates a new instance of EPurse */
public EPurse() { balance = (short)0;
pinCode = new OwnerPIN(EPURSE_PIN_TRY_LIMIT,
EPURSE_PIN_MAX_SIZE);
}

## Slide 57: OwnerPIN
Java Card 3.0 Programming
The CAD must validate the PIN code prior to access the other features
case EPURSE_ADD: apdu.setIncomingAndReceive(); if(!pinCode.isValidated())
ISOException. throwIt(
ISO7816.SW_SECURITY_STATUS_NOT_SATISFIED);
break;
case EPURSE_PIN: apdu.setIncomingAndReceive(); if(!pinCode.check(buffer,
ISO7816.OFFSET_CDATA, EPURSE_PIN_MAX_SIZE))
ISOException.throwIt(
ISO7816.SW_SECURITY_STATUS_NOT_SATISFIED);
break;

## Slide 58: OwnerPIN
Java Card 3.0 Programming
The OwnerPIN proposes a method to unblock a blocked PIN code (after a TRY_LIMIT unsuccessful attempts)
case EPURSE_UNBLOCK:
pinCode.resetAndUnblock();

## Slide 59: OwnerPIN
Java Card 3.0 Programming
The OwnerPIN proposes a method to reset the
validated flag
public boolean select(){ pinCode.reset();
}

## Slide 60: Conclusion
Java Card 3.0 Programming
●
In this chapter, we have seen
●
●
●
●
●
An introduction to the Java Card system What is a Java Card Applet
What is the Java Card Runtime Environment The lifecycle of an Applet
How to protect access with an OwnerPIN

## Slide 61
Cours 3: The key rules for Javacard Programming
Java Card 3.0 Programming

## Slide 62: Java Card Programming Issues
Reduced language Reduced library
Most exciting features of Java available in Java Card
Most difficulties coming from the ISO7816 protocol hidden by the JCRE and the API
Java Card 3.0 Programming
●
Programming a Java Card seems simple
●
●
●
●

## Slide 63: Java Card Programming Issues
Java Card 3.0 Programming
●
Powerful tools help developing applets
●
Basic toolkit available for free from Sun (Oracle)
–
Helps testing and debugging applets
●
Enhanced toolkits provided by most of the manufacturers to
–
–
Upload applets in target Java Cards Test, on board, the uploaded applets

## Slide 64: Java Card Programming Issues
No consistency in data when the card is teared suddenly from the reader
Poor usability and security
Time out and memory issues not taken in account
Java Card 3.0 Programming
●
Most of the trainee’s applets suffer from the following drawbacks:
●
●
●

## Slide 65: Tr U S T Me
Java Card 3.0 Programming
●
A Java Card applet must be
●
●
●
●
●
Transaction aware
Usable Secure
Time-out aware
Memory aware

## Slide 66: Transaction aware
●
Context
●
●
Memorize the ten last operations for an e- purse
Operation is qualified by
–
–
–
The type The amount The date
Java Card 3.0 Programming

## Slide 67: Transaction aware (code example)
Java Card 3.0 Programming
case EPURSE_ADD: apdu.setIncomingAndReceive(); if(!pinCode.isValidated())
ISOException.throwIt(
ISO7816.SW_SECURITY_STATUS_NOT_SATISFIED);
amount = Util.getShort(buffer, ISO7816.OFFSET_CDATA); balance = (short)(balance + amount);
list.add(buffer, ISO7816.OFFSET_INS,
ISO7816.OFFSET_CDATA, (short)2, (short)(ISO7816.OFFSET_CDATA + (short)2),
(short)8);
break;

## Slide 68: Transaction aware (a better code)
Java Card 3.0 Programming
…
try{
JCSystem.beginTransaction();
amount = Util.getShort(buffer, ISO7816.OFFSET_CDATA); balance = (short)(balance + amount);
list.add(buffer, ISO7816.OFFSET_INS, ISO7816.OFFSET_CDATA, (short)2, (short)(ISO7816.OFFSET_CDATA + (short)2),
(short)8);
JCSystem.commitTransaction();
}catch(TransactionException ex){ … }
break;

## Slide 69: Usability
●
Context
●
On an e-purse, each operation must be accepted only if the user’s PIN code had been validated and if the operation is possible
Java Card 3.0 Programming

## Slide 70: Usability (code example)
Java Card 3.0 Programming
case EPURSE_ADD: apdu.setIncomingAndReceive();
if(! pincode.check(buffer, ISO7816.OFFSET_CDATA, (byte)2)) ISOException.throwIt(ISO7816.SW_SECURITY_STATUS_NOT_SATISFIED);
amount =
Util.getShort(buffer, (short)(ISO7816.OFFSET_CDATA + (short)2)); balance = (short)(balance + amount);
list.add(buffer, ISO7816.OFFSET_INS,
(short)(ISO7816.OFFSET_CDATA + (short)2), (short)2, (short)(ISO7816.OFFSET_CDATA + (short)4),
(short)8);
break;

## Slide 71: Usability
Java Card 3.0 Programming
●
PIN code must not be checked at each operation
●
But at each session starting
●
PIN code must be deselected after the applet had been also deselected

## Slide 72: Security
●
Context
●
●
Iris scan security system with the card holder’s iris characteristics in a smart card
Problem:
–
Which part of the system must decide if the iris scanned
corresponds to the data stored in the smart card:
●
●
The card acceptance device? The Java Card?
Java Card 3.0 Programming

## Slide 73: Security (proposed answers)
Java Card 3.0 Programming
●
Answer 1:
●
●
The scanned data are passed to the smart card which returns yes or no!
Answer 2:
●
The Card Acceptance Device get the stored data from the card to compare it with the scanned data

## Slide 74: Security
Java Card 3.0 Programming
●
●
Mutual authentication is needed prior any data exchange
Card Acceptance Device
●
which is more difficult to replace by a forged one
must make the comparison between data stored in the card and the data scanned

## Slide 75: Time out
●
Context
●
●
A message is sent to the Java Card to be encrypted using a first command
A second command must be issued to get back the encrypted message
Java Card 3.0 Programming

## Slide 76: Time out (time issues)
Java Card 3.0 Programming
●
What if
●
●
The Java card is teared from the card reader after the first command arrives and before the second command is issued
Or if
●
The second command arrives before the first one is issued

## Slide 77: Time out
Java Card 3.0 Programming
●
Time out aware applet
●
●
Must blank the message to be encrypted if deselect and/or select is called before the second command is issued
Must refuse the second command if the first was not sent before

## Slide 78: Memory aware
●
Context
●
●
Memorize the ten last operations for an e-purse Operation is qualified by
–
–
–
The type The amount The date
Java Card 3.0 Programming

## Slide 79: Memory aware (code example)
case EPURSE_ADD: apdu.setIncomingAndReceive();
amount = Util.getShort(buffer, ISO7816.OFFSET_CDATA); Operation op = new Operation(buffer,
ISO7816.OFFSET_INS,ISO7816.OFFSET_CDATA, (short)2,
(short)(ISO7816.OFFSET_CDATA + (short)2), (short)8); list.add(op);
break;
Java Card 3.0 Programming

## Slide 80: Memory aware
Avoid creating object on the fly
Create all the objects needed during construction phase
Recycle already created objects
Java Card 3.0 Programming
●
More Memory aware code
●
●
●

## Slide 81: Conclusion
Java Card 3.0 Programming
●
At the beginning, smart card programming was done:
●
●
●
In assembly language At a low level
By engineers aware of the
–
–
–
–
–
Transactions Usability Security Time-out
Memory usage

## Slide 82: Conclusion
Java Card 3.0 Programming
●
Today, thanks to Java Card, applet programming can be done:
●
●
●
In Java
At a high level
By simple Java programmers

## Slide 83: Conclusion
Java Card 3.0 Programming
●
The Java Card programmers must be aware of:
●
●
●
●
●
Transactions Usability Security Time out
Memory usage

## Slide 84: Cours 4: Security
Smart cards tutorial
Hardware and software aspects

## Slide 85: Objectives
In this chapter, we'll see
  An introduction about the security aspects of the smart cards
    From a hardware point of view
    From a software point of view
Smart cards tutorial

## Slide 86: Hardware security
A smart card contains important data
  It could contain
    money (Electronic purses)
    Keys (EMV Credit Card)
    Sensitive Info (Fingerprint)
It must be tamper resistant
"If you know the attack you can build the shield"
Smart cards tutorial

## Slide 87: The attacks
X raying the micro-chip
Measuring the power consumption variation during critical APDU
  When the PIN code is transmitted for example
Measuring the answer delay
  To try to predict what branches in the program are completed
Smart cards tutorial

## Slide 88: The Counter Measure
The micro-chip uses an internal shield to protect itself against an X-Ray scanning
It guarantees the same delay for both branches of an alternative statement
It guarantees the same power consumption in all cases
Introduce lure (Random delay, fake processing)
Smart cards tutorial

## Slide 89: Software attacks and shields
•
Data are protected using cryptography
Various techniques
  DES, DES3, AES
  RSA, ECC
  SHA
Cryptography is based on
  A public algorithm
  A key
    Secret (DES, DES3, AES)
    Private/Public (RSA,ECC)
Smart cards tutorial

## Slide 90: Symmetric Enciphering
SAME KEY
Bob
Alice
Smart cards tutorial

## Slide 91: Symmetric Enciphering
Smart cards tutorial
encryptedData = f(K ,message)
message= f (K, encryptedData )
-1
ENCRYPTION:
f is the cryptographic function
K is the secret key
Message : the message to encrypt
DECRYPTION:
The most popular crypto algorithm used in SmartCard is 3DES (Data Encryption system) and
AES (Advence d Encryption Standard)
Same key

## Slide 92: Asymmetric enciphering
Bob’s Public Key (encryption key)
Alice
Bob’s private key (decyrption key)
Bob
Smart cards tutorial

## Slide 93: Asymmetric enciphering
Smart cards tutorial
encryptedData = f (PublicKey , message)
message = f (PrivateKey , encryptedData )
Different key
-1
f is the cryptographic function
PublicKey & PrivateKey is the key pair
Message : the message to encrypt
PublicKey : used to encrypt
PrivateKey : used to decrypt
The most popular crypto algorithm used in SmartCard is RSA
(https://fr.wikipedia.org/wiki/Chiffrement_RSA)

## Slide 94: Signing using asymmetric keys
Bob’s Public Key
Alice
Bob’s private key
Bob
Smart cards tutorial

## Slide 95: Signing using asymmetric keys
Smart cards tutorial
signature= sign(PrivateKey, dataToSign)
boolean = verify(PublicKey , encryptedData , dataToSign)
PublicKey & PrivateKey is the key pair
datatoSign: the message to sign
PublicKey : used to encrypt
PrivateKey : used to decrypt
The most popular crypto algorithm used in SmartCard is RSA
(https://fr.wikipedia.org/wiki/Chiffrement_RSA)

## Slide 96: Certify public key
X509 Certificate
•Subject (name, company, e-mail …)
•Issuer’s subject
•Public Key
Smart cards tutorial

## Slide 97: Certification Authority
Certificate
•Subject (name, company, e-mail …)
•Start Date
•End Date
•Issuer’s subject
•Public Key
Self Signed
Certificate
•Subject (name, company, e-mail …)
•Start Date
•End Date
•Issuer’s subject
•Public Key
Certificate
•Subject (name, company, e-mail …)
•Start Date
•End Date
•Issuer’s subject
•Public Key
Certificate
•Subject (name, company, e-mail …)
•Start Date
•End Date
•Issuer’s subject
•Public Key
Thawte, Verisign,
...
Smart cards tutorial

## Slide 98
Authentication
Smart cards tutorial
Privacy
Authorization
Integrity
Non-repudiation

## Slide 99: Protect private key With Smart cards
Smart cards tutorial
•
The Private key is born, lives and dies inside the card
Key pair generation
Secure access
Cryptographic algorithm process inside the card
Physically secure
  No hard drive storage of the private key
Portable
  No multi-key
  Multiple Device
Enciphering is done inside the card
  Computer Independent

## Slide 100: Hashing
8365923334
Modifying one bit completely changes the Hash
•Hash result is completely unpredictable
Hash
Standard algorithm is now SHA256, MD5 and SHA-1 are obsolete
Document
Smart cards tutorial

## Slide 101: Digital Signature (Email)
Letter
8365923334
Hash
=?
Identification/ Authentication of the content of the
letter
X.509
Certificate Authority
CA Public key (certificate checked)
Sender
Receiver
Kps
Sender's PK
X.509
Kss
Sender's SK
Sender’s private
key & X509
certificate
8365923334
Hash
Digital Signature
8A!G@3&04
X.509
Signing
Letter
Smart cards tutorial

## Slide 102: S/MIME Encryption
- generate "symmetric document key" (PC)
- encrypt "sym document key" with receiver’s public key
Message
Sender
Receiver
Trust Centre
Kpr
X.509
- get certificate of receiver, verify certificate and extract public key
- encrypt message with symmetric key (PC)
Encrypted message
$@/!&@#
- unwrap document key with the receiver’s private key
- decrypt message
with " sym document key
Message
Smart cards tutorial

## Slide 103: Example
Smart cards tutorial

## Slide 104: Example
Smart cards tutorial

## Slide 105: Example
Smart cards tutorial

## Slide 106: Example
Smart cards tutorial

## Slide 107: Example
Smart cards tutorial

## Slide 108: Example
Smart cards tutorial

## Slide 109: Example
Smart cards tutorial

## Slide 110: Example
Smart cards tutorial

## Slide 111: Example
Smart cards tutorial

## Slide 112: Encrypting w/public
Smart cards tutorial

## Slide 113: Result
Smart cards tutorial
CLA: | 80, | INS: | b2, P1: 00, P2: 00, Lc: 10, | 
00, | 01, | 02, | 03, | 04, | 05, | 06, | 07, | 08, | 09, | 0a, | 0b, | 0c, | 0d, | 0e, | 0f,
Le: | 40, |  |  |  |  |  |  |  |  |  |  |  |  |  | 
66, | ff, | e8, | 04, | 8a, | 41, | 9e, | c2, | dd, | e7, | 44, | 08, | a5, | 41, | c2, | e5,
79, | 3d, | 65, | 31, | a5, | c6, | c8, | 54, | bd, | 49, | 52, | eb, | d3, | 65, | 0e, | b6,
da, | 99, | f0, | e4, | 89, | b6, | 08, | a4, | f6, | 64, | f9, | 3d, | ba, | bb, | 93, | 61,
f8, | a4, | 95, | 3a, | 13, | 2d, | 17, | 73, | 7b, | 4c, | 49, | 27, | 9f, | 1e, | 8c, | 9c,
SW1:90,
SW2:00
CLA: | 00, | INS: | a4, P1: 04, P2: 00, Lc: 06, b6, 84, 89, 33, 88, 8E, 8F Le:00
SW1: | 90, | SW2: | 00

## Slide 114: Conclusion
In this chapter, we have seen
  An introduction about the security aspects of the smart cards
    From a hardware point of view
    From a software point of view
Smart cards tutorial

## Slide 115: SIM Cards
Smart cards tutorial
Proactive SIM cards

## Slide 116: Introduction
The standards driving the smart cards for mobile telephony
What is the SIM Toolkit
How Java Card handles the SIM toolkit
A full example of a Java Card applet built using the SIM Toolkit library
Smart cards tutorial
●
In this chapter, we'll see
●
●
●
●

## Slide 117: SIM cards
•
Standardized by ETSI for GSM
• GSM 11.11 V6.1.0
  SIM specs
    Subscriber Identification Module
GSM 11.14 V7.1.0
  SIM Toolkit specs
• GSM 03.19 V1.0.0
  Javacard SIM API
Smart cards tutorial

## Slide 118: SIM cards
The SIM Card is used to authenticate the subscriber to the operator network
The SIM Card contains network operator configuration
Smart cards tutorial

## Slide 119: Proactives SIM
Using the SIM Toolkit, possibility to
  Program the SIM
  Make the SIM card application driving the phone
    Access to keyboard, display, …
Smart cards tutorial

## Slide 120: Internal organization
The SIM contains a certain number of "files" grouped into "directories"
Terminology:
  Element File: file
  Dedicated File: directory
Root 0x3F00
File 0x2222
Directory 0x2345
File 0x2A34
Smart cards tutorial

## Slide 121: File hierarchy
Smart cards tutorial

## Slide 122: File hierarchy
Smart cards tutorial

## Slide 123: Proactive SIM
The ISO7816 standard does not permit that the card starts talking first
– A card is waiting for an APDU and responds when it receives the APDU
Proactive SIM cards use a specific status word to indicate to the Mobile Equipment that they want to talk to it
Smart cards tutorial

## Slide 124: Proactive protocol
Smart cards tutorial

## Slide 125: Allowed commands for the SIM
The SIM card can
  Display text on the phone display
  Prompt User to input data from the keyboard
  Play tone
  Send a SMS
  Process an incoming SMS
– …
Smart cards tutorial

## Slide 126: SIM Toolkit applet
Smart cards tutorial
A SIM Toolkit applet must
  Import sim.access and sim.toolkit packages
  Extend the javacard.framework.Applet
  Implement the interfaces
    ToolkitInterface
    ToolkitConstants

## Slide 127: SIM Toolkit applet
Smart cards tutorial
Example:
import import import
sim.toolkit.*; sim.access.*; javacard.framework.*;
public
class MyApplet1 extends javacard.framework.Applet implements
ToolkitInterface, ToolkitConstants {
// Mandatory variables
private SIMView gsmFile;
private ToolkitRegistry reg;

## Slide 128: SIMView
Smart cards tutorial
The SIMView interface is the interface between the applet and the GSM filesystem
It proposes
  Constants to identify in a simple way the regular GSM files
  Methods to access these files

## Slide 129: SIMView
Smart cards tutorial
= (short)0x7F10;
: DF TELECOM = 0x7F10 */
short FID_DF_TELECOM
: DF GSM = 0x7F20 */
short FID_DF_GSM
= (short)0x7F20;
= (short)0x7F21;
: DF DCS-1800 = 0x7F21 */
short FID_DF_DCS_1800
: DF IS-41 = 0x7F22 */
short FID_DF_IS_41
= (short)0x7F22;
Example:
/** DF under MF */
/** File identifier public static final
/** File identifier public static final
/** File identifier public static final
/** File identifier public static final
/** File identifier
: DF FP-CTS = 0x7F23 */

## Slide 130: SIMView
Smart cards tutorial
fid, byte fci[], fciOffset,
fciLength) throws
Example:
public short select(short
short short
ArrayIndexOutOfBoundsExceptio; SIMViewException, NullPointerException,

## Slide 131: SIMSystem
Smart cards tutorial
The SIMSystem class provides one method which is
– SIMView
getTheSIMView()

## Slide 132: ToolkitRegistry
Smart cards tutorial
The SIM Applet communicates with the mobile equipment through the ToolkitRegistry
The SIM applet get an entry from the
ToolkitRegistry in order
  To receive and process the events sent by the mobile equipment
  To send command to the mobile equipment

## Slide 133: SIM Toolkit applet
Smart cards tutorial
Example
// Main private private
Menu
byte idMenu1;
byte[] Menu1;
public MyApplet1() {
// Get the GSM application reference gsmFile = SIMSystem.getTheSIMView();
// Get the reference of the applet ToolkitRegistry object reg = ToolkitRegistry.getEntry();
/**@todo: Customize your menu titles here*/
Menu1 = new byte[] { (byte) '1', (byte) ' ', (byte) 'M', (byte) 'e',
(short) 0, (short) Menu1.length, 0, (short) 0);
(byte) 'n', (byte) 'u', (byte) '1' };
// Define the applet Menu Entry idMenu1 = reg.initMenuEntry(Menu1, PRO_CMD_SELECT_ITEM, false, (byte)
}

## Slide 134: initMenuEntry
Smart cards tutorial
public byte initMenuEntry(
byte[] menuEntry,
short offset,
short length,
byte nextAction,
boolean helpSupported, byte iconQualifier, short iconIdentifier
// the menu entry string
// its offset
// its length
// next action to execute when
menu is selected
// true if help available
// 0 is no icon
)
throws java.lang.NullPointerException, java.lang.ArrayIndexOutOfBoundsException, ToolkitException,
TransactionException

## Slide 135: SIM Toolkit applet
Smart cards tutorial
/**
Method
@param
@param
@param
called by the JCRE at the installation of the applet bArray the byte array containing the AID bytes bOffset the start of AID bytes in bArray
bLength the length of the AID bytes in bArray
*/
public static void install(byte[] bArray, short bOffset, byte bLength) {
// Create the Java SIM toolkit applet
MyApplet1 StkCommandsExampleApplet = new MyApplet1();
// Register this applet StkCommandsExampleApplet.register(bArray, (short) (bOffset + 1), (byte) bArray[bOffset]);
}

## Slide 136: SIM Toolkit applet
/**
Method called by the SIM Toolkit Framework
@param event the byte representation of the event triggered
*/
public void processToolkit(byte event) {
// Manage the request following the MENU SELECTION event type
if (event == EVENT_MENU_SELECTION) {
// Get the selected item
EnvelopeHandler envHdlr = EnvelopeHandler.getTheHandler();
byte selectedItemId = envHdlr.getItemIdentifier();
// Perform the required service following the Menu1 selected
// item
if (selectedItemId == idMenu1) { menu1Action();
}
Smart cards tutorial

## Slide 137: SIM Toolkit applet
private byte [] helloWorld;
private void menu1Action() {
// Get the received envelope
ProactiveHandler proHdlr = ProactiveHandler.getTheHandler(); helloWorld = new byte[]{(byte)'H',(byte)'e',(byte)'l',(byte)'l',
(byte)'o',(byte)' ',(byte)'w',(byte)'o',(byte)'r',(byte)'l',(byte)'d'};
// Initialize the display text command
proHdlr.initDisplayText((byte) 0x00, DCS_8_BIT_DATA, helloWorld, (short) 0, (short) (helloWorld.length));
proHdlr.send();
return;
}
Smart cards tutorial

## Slide 138: Running
Smart cards tutorial

## Slide 139: Documentation
Smart cards tutorial
More documentation in
– 3gpp 43019-560

## Slide 140: Conclusion
The standards driving the smart cards for mobile telephony
What is the SIM Toolkit
How Java Card handles the SIM toolkit
A full example of a Java Card applet built using the SIM Toolkit library
Smart cards tutorial
●
In this chapter, we have seen
●
●
●
●

## Slide 141
Smart Card Web Server
An other way for the SIM card to control the handset
Smart cards tutorial

## Slide 142: Introduction
A new approach to interface the applications in the SIM card, using the handset
The architecture of the SCWS
A full application for a SIM card supporting SCWS
Smart cards tutorial
●
In this chapter, we'll see:
●
●
●

## Slide 143: Introduction
Smart cards tutorial
●
SIM Toolkit was introduced at the time when handset had few capabilities for interfacing
●
●
●
Text oriented display No graphics Hierachical menus
●
Modern handsets support
●
●
Full color graphic interface Point and pin menus

## Slide 144: Introduction
Smart cards tutorial
●
Gemalto developers proposed at Cartes 2000 a simplified web server inside the SIM card
●
With
●
●
the introduction of the USB port and TCP/IP stack
the powerfulness of modern SIM card (32bits, NAND Flash)

## Slide 145: SCWS
Smart cards tutorial
●
●
The standard adopted is called:
Smart Card Web Server This standard supposes
●
A TCP/IP link
–
On USB
●
A TCP/IP stack on board

## Slide 146: SCWS
SCWS
Java Virtual Machine
Low Level Resources
Javacard APIs
SCWS API
STK Api
Applets
Smart cards tutorial

## Slide 147: Packages and classes
/*
* Imported packages
*/
Import javacard.framework.*;
Import uicc.scws.HttpRequest;
Import uicc.scws.HttpResponse;
Import uicc.scws.ScwsConstants;
Import uicc.scws.ScwsException;
Import uicc.scws.ScwsExtension;
Import uicc.scws.ScwsExtensionRegistry;
Universal Integrated Circuit Card
Smart cards tutorial

## Slide 148: ScwsConstants
Smart cards tutorial
MIME types
  CONTENT_TYPE_IMAGE_GIF
  CONTENT_TYPE_TEXT_HTML
Status code
– SC_OK (200)
  SC_NOT_FOUND (404)
Parsing tags
  URI_QUERY_TAG

## Slide 149: ScwsExtension
Smart cards tutorial
The applet (servlet!) working in SCWS mode must implement ScwsExtension
That means overiding the methods
  doGet()
  doPost()
  doHead()
– ...

## Slide 150: HttpRequest
Smart cards tutorial
Not really the J2EE HttpRequest but enough to extract data from a HTTP request
Provides methods like
  findAndCopyKeywordValue
  getContentLength
  getContentType

## Slide 151: HttpResponse
Smart cards tutorial
As for HttpRequest, helps the user to provide an HTTP response to the request
Provides methods like
  setContentType()
  appendContent()
  writeStatusCode()
  flush()

## Slide 152: Example
Smart cards tutorial
In the next servlet, the strings are encoded as arrays of bytes
– Strings are not supported by Java Card 2
In the next two pages, the pseudo code written in comment show how the servlet would be written if String was supported by this release of Java Card

## Slide 153: Example
Smart cards tutorial
/*
public class HelloWorld extends javacard.framework.Applet implements AppletEvent, ScwsExtension {
public final static String url = "/HelloWorld"; public final static String appId = "HelloWorld;
public byte[] temporaryBuffer;
public final static short TEMPORARY_BUFFER_LENGTH = (short) 100;
public final static String HTML_BEGIN = "<html>"+"<head>"+
"<title>"+"Hello"+"</title>"+"</head>"+
"<body BGCOLOR=\"#FFFFFF\">"+"<center>"; public final static String HELLO = "Hello ";
public final static String HTML_END = "</center>"+"</body>"+ "</html>"

## Slide 154: Example
Smart cards tutorial
Unfortunately String are not yet supported by Java Card
– Strings are supported by Java Card 3
The arrays of bytes are not so easy to read, but the result is the same

## Slide 155: Example
public class HelloWorld extends javacard.framework.Applet implements AppletEvent, ScwsExtension {
/** the servlet url */
public final static byte[] url = { (byte)'/', (byte)'H', (byte)'e', (byte)'l', (byte)'l', (byte)'o', (byte)'W', (byte)'o', (byte)'r', (byte)'l', (byte)'d' };
public final static byte[] appId = { (byte)'H', (byte)'e', (byte)'l', (byte)'l', (byte)'o', (byte)'W', (byte)'o', (byte)'r', (byte)'l', (byte)'d' };
Smart cards tutorial

## Slide 156: Example
(byte)'<',(byte)'h',(byte)'t',(byte)'m',(byte)'l',(byte)'>',
(byte)'<',(byte)'h',(byte)'e',(byte)'a',(byte)'d',(byte)'>',
(byte)'<',(byte)'t',(byte)'i',(byte)'t',(byte)'l',(byte)'e',(byte)'>',
(byte)'H',(byte)'e',(byte)'l',(byte)'l',(byte)'o',
(byte)'<',(byte)'/',(byte)'t',(byte)'i',(byte)'t',(byte)'l',(byte)'e', (byte)'>',
(byte)'<',(byte)'/',(byte)'h',(byte)'e',(byte)'a',(byte)'d',(byte)'>',
Smart cards tutorial
// Temporary operation buffer
public public public
byte[] temporaryBuffer;
final static short TEMPORARY_BUFFER_LENGTH = (short) 100; final static byte[] HTML_BEGIN = {

## Slide 157: Example
Smart cards tutorial
(byte)'<',(byte)'b',(byte)'o',(byte)'d',(byte)'y',(byte)' ',
(byte)'B',(byte)'G',(byte)'C',(byte)'O',(byte)'L',(byte)'O',(byte)'R',
(byte)'=',(byte)'"',(byte)'#',(byte)'F',(byte)'F',(byte)'F',(byte)'F', (byte)'F',(byte)'F',(byte)'"',(byte)'>',
(byte)'<',(byte)'c',(byte)'e',(byte)'n',(byte)'t',(byte)'e',(byte)'r', (byte)'>'};
public final static byte[] HELLO ={(byte)'H',(byte)'e',(byte)'l',
(byte)'l',(byte)'o',(byte)' '};
public final static byte[] HTML_END = {
(byte)'<',(byte)'/',(byte)'c',(byte)'e',(byte)'n',(byte)'t',(byte)'e', (byte)'r',(byte)'>',
(byte)'<',(byte)'/',(byte)'b',(byte)'o',(byte)'d',(byte)'y',
(byte)'<',(byte)'/',(byte)'h',(byte)'t',(byte)'m',(byte)'l',(byte)'>'};

## Slide 158: Example
Smart cards tutorial
public HelloWorld(byte[] buffer, short offset, byte length) {
// First LV is instance AID
short aid = offset;
offset += buffer[offset] + (byte) 1;
// LV is Privilege
offset += buffer[offset] + (byte) 1;
// Third LV is specific install parameter (extract from TAG C9)
offset ++;
// Register the new applet instance to the JCRE
register(buffer, (short) (aid + (short) 1), buffer[aid]);
// Run/Debug configuration for URL Mapping ScwsExtensionRegistry.register(this, appId, (short) 0,
(short) appId.length);

## Slide 159: Example
Smart cards tutorial
try {
// Create a temporary buffer for read/write temporaryBuffer = JCSystem.makeTransientByteArray( TEMPORARY_BUFFER_LENGTH, JCSystem.CLEAR_ON_RESET);
} catch (SystemException se) {
// create buffer in persistent memory as not enough transient
// is available
temporaryBuffer = new byte[TEMPORARY_BUFFER_LENGTH];
}

## Slide 160: Example
Smart cards tutorial
public void doGet(HttpRequest req, HttpResponse resp) throws ScwsException {
try {
resp.writeStatusCode(ScwsConstants.SC_OK); resp.setContentType(ScwsConstants.CONTENT_TYPE_TEXT_HTML); resp.enableChunkMode();
short queryLength = req.findAndCopyKeywordValue( ScwsConstants.URI_QUERY_TAG, temporaryBuffer,(short)0, (short)temporaryBuffer.length);
resp.appendContent(HTML_BEGIN,(short)0,(short)HTML_BEGIN.length); resp.appendContent(HELLO, (short)0, (short)HELLO.length); resp.appendContent(temporaryBuffer, (short)0, queryLength); resp.appendContent(HTML_END,(short)0, (short)HTML_END.length);
}catch(Exception e) {resp.writeStatusCode(ScwsConstants.SC_BAD_REQUEST);} resp.flush();

## Slide 161: Static HTML
Static HTML file : helloworld.html
HelloWorld</p>
<html>
<body>
<p>Simagin
<br>
<form action="/HelloWorld" method="get">
<input name="name" type="text"> <br>
<input value="Type in your name" type="submit">
</form>
</body>
</html>
URI of the SCWS servlet
Smart cards tutorial

## Slide 162: Running
Smart cards tutorial

## Slide 163: Conclusion
A new approach to interface the applications in the SIM card, using the handset
The architecture of the SCWS
A full application for a SIM card supporting SCWS
Smart cards tutorial
●
In this chapter, we have seen:
●
●

## Slide 164
Java Card 3.0 Connected Edition
A new and rich flavour of Java Card
Smart cards tutorial

## Slide 165: Introduction
The main enhancements introduced by Java Card 3
The restrictions of Java Card 3 compared to Java SE
A full example of a servlet
Smart cards tutorial
●
In this chapter, we'll see
●
●
●

## Slide 166: Features
Smart cards tutorial
●
Java Card 3.0 has two editions:
●
The Classic Edition
–
–
Compatible with Java Card 2 Applications are built with applets
●
The Connected Edition
–
–
With a WEB server embedded HTTP, TCP/IP over USB

## Slide 167: Features
Java Card 3.0 classic edition remains applet oriented
Java Card 3.0 connected edition is servlet oriented
Smart cards tutorial
●
●
●
Specifications of the supported servlets are extracted from the Servlet API Specifications 2.4
–
Everything which deals with floating point numbers, J2EE, etc. are not taken in account.

## Slide 168: Features
Smart cards tutorial
●
But, like traditionnal servlets, the Java Card 3 servlets support the methods:
●
●
●
●
●
●
●
doGet doPost doHead doPut doDelete doOptions doTrace

## Slide 169: Features
Smart cards tutorial
●
Better support of the Java language
●
●
●
●
●
●
All data types except float and double Multiple threads
Extensive API support (java.lang, java.util, GCF, and so on)
Direct handling of class files, with all loading and linking on card
All new Java language syntax constructs, like enums, generics, enhanced for loops, auto boxing/unboxing, and so on
Automatic garbage collection

## Slide 170: Architecture
Smart cards tutorial

## Slide 171: Architecture
Smart cards tutorial

## Slide 172: Example
The following example is created with NetBeans 6.9 with the Java Card wizard
It is the web instance of the very well known
« Hello world » program
Smart cards tutorial
●
●
●
Most code is automatically generated by the Java Card wizard

## Slide 173: Example
Smart cards tutorial

## Slide 174: Example
Smart cards tutorial

## Slide 175: Example
Smart cards tutorial

## Slide 176: Example
Smart cards tutorial

## Slide 177: Example
Smart cards tutorial

## Slide 178: Example
Smart cards tutorial

## Slide 179: Example
Smart cards tutorial

## Slide 180: Example
Smart cards tutorial

## Slide 181: Example
Smart cards tutorial

## Slide 182: Example
Smart cards tutorial

## Slide 183: Example
Smart cards tutorial

## Slide 184: Example
Smart cards tutorial

## Slide 185: Example
Smart cards tutorial

## Slide 186: Example
Smart cards tutorial

## Slide 187: Conclusion
The main enhancements introduced by Java Card 3
The restrictions of Java Card 3 compared to Java SE
A full example of a servlet
Smart cards tutorial
●
In this chapter, we have seen
●
●
●

## Slide 188
Conclusion
Smart cards tutorial

## Slide 189: Conclusion
Smart cards tutorial
●
●
●
In 1996, the Java Card system changed dramatically the way to program secure applications for smart cards
Despite many concurents on the field, this system remains today the first language for smart cards in the world
Combined with Java for Mobile Equipment it represents the solution to develop secure applications for the future powerful smartphones